FAITH

YACHT SPECIFICATION

TYPE	Twin Screw Displacement yacht

FLAG		Cayman Islands

DIMENSIONS	Length O.A.	96.55m (316ft)

Length W.L.		85.55m (280.9ft)

Beam	14.5m (47.7ft)

Draft (full load) 		3.75m (12.2ft)

TONNAGE	GT	<3,000 tonnes

YEAR BUILT	Delivered early 2017

BUILDER	Feadship, De Vries, The Netherlands

NAVAL ARCHITECT	De Voogt Naval Architects, The Netherlands

EXTERIOR DESIGNER	Redman Whiteley Dixon, United Kingdom

INTERIOR DESIGNER	Chahan, France

CONSTRUCTION	Steel hull

Aluminium superstructure

Teak laid decks

CLASSIFICATION	Lloyds +100A1 SSC Yacht Mono G6 +LMC UMS SCM ECO

LY3 Compliant

MACHINERY

MAIN ENGINES	2 x 2,240kW MTU diesel engines type 16V 4000 M63L

GEAR BOXES	2 x Reintjes 6:1 reverse reduction gear boxes with trailing oil pumps

SHAFTS & PROPELLERS	2 x Van Voodren 5-blade high skew propellers with 2.2m diameter connected to stainless steel shafts

SPEEDS 	Maximum contractual cruising speed of 17 knots (minimum)

Cruising speed approximately of 15 knots

Economical long range cruising speed of 12 knots

RANGE	5,000 nm @ 12 knots

AUXILIARY MACHINERY & ELECTRICAL SYSTEM

GENERATORS	3 x 450 kW Caterpillar diesel generators type C18 each producing 230-400V 50Hz

EMERGENCY GENERATOR	1 x 200 kW Caterpillar diesel generator type C9

ELECTRICITY	400V 3-phase 50 Hz

230V single phase 50 Hz (lighting, domestic equipment, control circuits and nautical equipment)

24V DC

SHORE POWER	1 x 450 kW Eekels Technology shore power converter type SPC-II Hybrid

BATTERIES	All batteries will be gel-cell type

TANK CAPACITIES (approximate)

FUEL 	264,850 litres (63,492 US gallons) approximately

WATER	75,000 litres (24,366 US gallons) approximately

WATERMAKERS	2 x HEM reverse osmosis watermaker type with capacity to produce approximately 2 x 21,000 litres a day

LUBE OIL	7,000 litres (1,585 US gallons) approximately

DIRTY LUBE OIL	8,620 litres (2,280 US gallons) approximately

GREY WATER	40,000 litres (6,605 US gallons) approximately

BLACK WATER	21,000 litres (3,698 US gallons) approximately

ANCILLARY EQUIPMENT

STEERING SYSTEM	2 x independent Becker rudders

SYNAMIC POSITIONING 	Navis dynamic positioning system type JP4000 with joystick controls from bridge driving both bow and stern thrusters

BOW THRUSTER	1 x 470kW Jastram bow thruster type BU 90F

STERN THRUSTER	1 x 250 kW Veth retractable azimuthing stern thruster

STABILIZERS	Quantum QC-2400 zero speed stabilizers with XT Fin Blades

FUEL FILTERS	Coalescer fuel filtration system

FUEL SEPERATOR	2 X Alfa Laval fuel separator

OIL/WATER SEPARATOR	1 x Boss Fuel/Water Separator type 107

FIRE/BILGE PUMP	2 x Azcue fire / emergency pump type CA 65/30

3 x Demsi bilge pumps type Vac 4001

SEWAGE TREATMENT	Hamann sewage treatment system type HL-Content Plus 10 (IMO compliant)

WC's	Jets vacuum WC system

AIRCONDITIONING	Heinen & Hopman custom multi zone air conditioning system

SAFETY & SECURITY EQUIPMENT

SAFETY	6 x 25 person and 1 x 6 person inflatable flat pack life rafts with SOLAS A-pack installed on bridge deck

1 x 4.5m SOLAS approved rescue boat

8 x orange ring buoys

Adult and child life jackets (per regulatory requirements)

Immersion suits (per regulatory requirements)

2 x Jotron GPIRB Tron-40GPS with automatic release

AIS

FIRE FIGHTING	Marioff HiFog high pressure water mist fire extinguishing system, to include:

HiFog sprinkler system with heat sensitive bulbs in spray heads in accommodation; Engine room and tender garage spray heads with manually operated valve; Galley hood and above deep fat fryer heads with locally operated valve (Section valves and test points as per Class requirements)

Sea water fire-fighting system

Fire extinguishers located throughout the Yacht

Smoke detectors

Fire hoses and nozzles

4 x fireman’s suits

4 x safety helmets

4 x complete BA system

4 x electric safety lamps

4 x long axe

4 x safety line with belt

4 x pairs of rubber boots and gloves

5 x emergency escape breathing device

ALARMS	Feadship standard digital alarm system

PA and general alarm system (operated from bridge)

Tyco fire, smoke and gas alarm system with heat and smoke detectors in all accommodation spaces, general areas, engine room, galley, pantry and crew mess

SECURITY	CCTV motion sensor and ship’s monitoring system of all external doors and hatches

Entrance Riviera gangway with buzzer and videophone

All entrance doors equipped with alarms connected to Yacht’s alarm system

COMMUNICATION EQUIPMENT GMDSS EQUIPPED & CERTIFIED

SATCOM	2 x FB500Fleet Broadband satellite communications terminals

2 x Sailor 900 VSAT with one hotspot antenna with several VLans configured for extra security

Satcom C with DSC

CELLULAR SYSTEM	2 x Quad-band GSM cellular units

VHF RADIOTELEPHONES	2 x Sailor VHF radiotelephones with DSC type SP Radio RT- 6222

3 x GMDSS approved VHF handheld radiotelephones

OTHER	VOIP telephone system

Cat-6 computer network extended throughout the Yacht

NAVIGATION EQUIPMENT

MAGNETIC COMPASS	1 x Cplath Jupiter magnetic compass installed in the deck head of the bridge

GYRO COMPASS	2 x Cplath Navigat gyro compass type Mk 1

AUTOMATIC PILOT	1 x Autopilot linked to DP system

Navis heading control system JP4000

LOG	Consilium speed log

ECHO SOUNDER	Consilium dual frequency Echo Sounder

RADAR	2 x Jotron radar transponders

2 x ARPA radars

#### ELECTRONIC CHARTS	Transas ECDIS charts

GPS	2 x SAAB DGPS receivers

WIND INSTRUMENTS	NMEA system wind and temperature station

DECK EQUIPMENT

ANCHOR WINDLASS	2 x Steen stainless steel vertical anchor windlasses each with vertical warping capstans

AFT WARPING CAPSTANS	2 x Muir stainless steel aft warping capstans type VC20000

GROUND TACKLE	2 x U2 grade galvanized steel anchors (minimum of 1,195kg each) connected to 2 x 220 metre U3 grade galvanized stainless steel stud link chains

BOAT CRANE & DAVITS	2 x Akerboom overhead crane beams in tender garage

1 x van Driel crew tender crane

1 x van Driel rescue tender crane

PASSERELLE 	Akerboom Riviera gangway

SIDE BOARDING LADDERS	Akerboom side boarding ladder

Portable self-levelling boarding ladder

SEARCHLIGHT	2 x Carlisle and Fitch night finder searchlights

AWNING	Sailtech awnings Bridge Deck, Owner’s Deck, Sun Deck, plus 8 independent sun parasols

AUDIO/VISUAL ENTERTAINMENT SYSTEMS

The specification of the audio/ video equipment has been prepared by Van Berge Henegouwen (VBH). Audio video equipment will consist of central fitted equipment in a specialised temperature controlled equipment rack room on the tank deck, providing audio and video to Owner’s and guest areas, and to crew areas.

SATELLITE 	2 x Sea Tel satellite receivers type 120 TVHDs

SYSTEM	Crestron Digital Media matrix supporting UHD and 4k

Kaleidescape audio and video on demand system controlled through Apple iPad Air 2s located throughout the Yacht

CINEMA	THX-standard cinema with Sony projector and 130” curved Stewart Filmscreen

TVs	23 x mostly Samsung LED televisions located throughout the Yacht (Particular highlights are a 95” television in the Bridge deck lounge, 85” in the owner’s suite and 90” in the Cosy lounge and a 75” on both the Owner’s deck aft and Bridge deck aft)

OFFICE EQUIPMENT

COMPUTERS	An integrated IT, CCTV, and VoIP system. All three systems will run on virtual servers which are hosted on 2 physical Cisco servers with separate RAID storage units. This ensures data is protected in case of a drive failure and servers can continue to run even in the case of a whole server failure.

PHOTOCOPIER/PRINTER	3 x A4 Xerox 6605 laser printers in Ship’s Office, Owner’s Office and Switchboard Room

DOMESTIC EQUIPMENT

MAIN GALLEY 	3 x Bohner induction hobs type BI 40K

2 x MKN Hansdapf Combisteamer type CGE-62 gold maxi

1 x IME pizza oven type Picolo 1

1 x Bohner frying plate type BG 50 E

1 x MKN salamander type Vario

2 x Foster refrigerators type EP 700 H

1 x Foster freezer type EP 700 L

1 x Manitowoc ice cube maker type EC 30

2 x Roland kuchen under counter refrigerator type KKS2108

1 x Irinox easy fresh blast freezer type EF 10.1

1 x ADE slicer type Juwel 1

1 x Vacumit vacumit machine type EST/20 LC

1 x Telme gelato/sorbet machine

1 x Panasonic microwave oven type NE-210

2 x Hobart dishwasher type Premax Fps-10A

1 x CB chicken grill type E-8N-S2

1 x Clage hydrotap type BC 100/125

LAUNDRY	3 x Miele washing machines type PW 6065 LP (ED), 6.5kg capacity

3 x Miele dryers type PT 7136 L (ED), 6.5kg capacity

2 x Miele washing machines type PW 6167 EL, 16 kg capacity

2 x Miele dryers type PT 8333 EL ED, 12-16 kg capacity

1 x Miele large roller ironer type HM 21-140

1 x Lelit ironing board type PA 027

1 x Lelit steam iron type PG027

1 x Electrolux drying cabinet type TS560

PANTRY (main deck)	1 x Nespresso coffee machine type CS 220 PRO

1 x Miele refrigerator type K9122Ui

1 x Hoszhisaki ice-cube maker type IM-30CNE

1 x Eurocave wine cooler type 3-zone E-pure-L

1 x Wine display

SALOON BAR (main deck)	1 x Sub Zero refrigerator type ICBID-30RP

1 x Sub Zero refrigerator/freezer type ICBID-30CI

PANTRY (bridge deck)	1 x Panasonic microwave oven type NE1027

1 x Nespresso coffee machine type CS 220 PRO

1 x Miele refrigerator type K9122Ui

1 x Hoszhisaki ice-cube maker type IM-30CNE

PANTRY (owner’s deck)	1 x Panasonic microwave oven type NE1027

1 x Nespresso coffee machine type CS 220 PRO

1 x Miele refrigerator type K9122Ui

1 x Hoszhisaki ice-cube maker type IM-30CNE

SUN DECK PANTRY	1 x Hoszhisaki ice-cube maker type IM-30CNE

SUNDECK	1 x ‘The Stone Bake Oven Company’ stone bake oven type Mezzo 76

1 x Luxor charcoal grill type AHT-30CHAR-BI-OT

2 x Frigonautica refrigerator type FRS115RC

BEACH CLUB	2 x Frigonautica refrigerator type FRS130RC

1 x Frigonautica freezer type CS130C

1 x Hoszhisaki ice cube maker

CREW MESS	1 x Panasonic microwave oven type NE1027

1 x Nespresso coffee machine type CS 220 PRO

2 x Electrolux refrigerator type 691174

2 x Miele dishwasher type PG 8056 U Speed

OTHER	Cold storage room

Glass crusher

Trash compactor

Gobi 50 food waste processor

OTHER EQUIPMENT

HELIDECK	Forward on the bridge deck with hatch to hangar below.  Approved for take-off and landing of Eurocopter EC145 and Bell 429 (under investigation) with removable or foldable tail and foldable blades  Maximum weight of 4,000kg and a maximum overall dimension “D” of 13.1m.

Fuelling station (approx. 2,000 litres) next to hangar.

### POOLS		Large Swimming Pool on main deck aft with dimensions: 9m x 3.6m with waterfall

Jacuzzi dip pool on sun deck forwards

SHIP'S SAFES		Safes in each Stateroom, Owners office and Captain’s cabin

BARBEQUE	Luxor charcoal grill on sun deck

PIZZA OVEN		Pizza oven on sun deck

GYM EQUIPMENT		1 x Life Fitness Integrity Series Elliptical Crosstrainer

1 x Technogym Strength Training Equipment

1 x CycleOps 300 Pro Exercise Bike

Technogym Free Weights

Technogym ARKE Kit

Freemotion Cable Column

TENDERS & WATERSPORTS EQUIPMENT

TENDERS	1 x 10m Custom Feadship Limousine tender

1 x 10m Custom Feadship Open tender

1 x 7m Custom X-Craft Crew tender

1 x 5.7m Custom X-Craft Crew tender

1 x Zodiac 4.5m Rescue boat

ACCOMMODATION

VERTIGO accommodates up to 14 guests, in 7 cabins, with an additional 4 staff in 2 convertible cabins.

OWNER	Dedicated Owner’s Deck with a full width suite forward with his and hers en suite bathrooms (hers with a bathtub and his with a luxury steam shower) and dressing rooms.

The Cosy Lounge leads to an exterior area with seating, dinning and a fire pit.

GUESTS	Four double Guest cabins and two VIP’s on the main deck, each with en suite bathroom and dressing room.

Two twin staff cabins on the bridge deck starboard (optional guest cabins). These staff cabins share one bathroom.

CREW	Accommodation for 34 crew in total

Captain’s double cabin on the bridge deck

4 x Officer single cabins

Separate Doctor and Pilot single cabins (the pilot cabin also has a Pullman bunk)

13 x twin bunk cabins

These particulars have been prepared by us from information provided by the sellers and are intended as a general guide to the vessel. We cannot, however, be liable for any inaccuracy. It is up to the purchaser to confirm details of concern to him by survey, inspection and/or enquiry of the seller and to ensure that the purchase contract properly reflects his concern and specific details upon which he may rely. We always advise an independent survey.